## Slide 1: Colombo előtt sem ismert izotópok a vízben
Palcsu László
Izotópklimatológiai és Környezetkutató Központ (IKER)
Magyar Tudományos Akadémia
Atommagkutató Intézet

## Slide 2
Elemek, izotópok vízben:
3H, δ2H
3H/1H=10-18
δ17,18O
δ17,18O
14C/12C=10-12
δ15N (NO3-,NH4+)
3He/4He
He
Ne, Ar, Kr, Xe

## Slide 3
What does (apparent) water age mean ?
What is mean residence time?
What is transit time?
What do we have to mean in age distribution?
What do all these give us?
Water age is a quantity with a dimension of time, and it helps us estimate the age distribution (end hence other important parameters of the aquifer: volume, mixing patterns, response time, etc.).
The point:
The more age indicators we know, the better estimation to the age distribution can be made

## Slide 4
Methods for water age detemination
(time range: 0 to many millions of years)
This is what we perform
This is what we perform
This is what we WILL perform
This is what we WILL perform
We WILL perform sampling and krypton separation (measurement by ATTA)
SF6 (CFCs?)

## Slide 5
Methods for water age detemination (time range: 0-60 years)

## Slide 6
39Ar (argon-39):
Pure beta-decaying isotope
Half-life: 269 years (±3)
Cosmogenic isotope (40Ar (n,2n)39Ar)
Activity concentration: 1.5 mBq/litreAr (stable initial concentration over time)
39Ar/Ar  10-16 (this is the main problem)
gas exchange
sampling well
unsaturated zone
saturated zone
impermeable layer
equilibration
The only 2 (+1) laboratories:
University of Bern, Switzerland
PNNL, Richland, USA
(ICER, Debrecen, Hungary)

## Slide 7
85Kr in the atmosphere: from reprocessing plants

## Slide 8
39Ar and 85Kr dating of water: sampling in the field:
The aim is to extract at least 100 litres dissolved gas from the water
(and sampling for 81Kr)
Thomas Reichel PhD dissertation

## Slide 9
Argon (and krypton) separation: 1 litre of Ar (99.99% purity)!
Cryogenic gas chromatography
Thomas Reichel PhD dissertation

## Slide 10
39Ar detection: low background proportional counting tubes
(we choose this)
modern argon: 1.5 mBq/liter!
130 desintegration/day (at least two weeks of detection is necesarry!)
Shielding:
Rock (at least 30 m)
Boronated paraffin (10 cm)
Lead (10 cm)
Copper (1 cm)
Guard counter

## Slide 11
39Ar detection: low background proportional counting tubes
Ar counter gas: 90% argon + 10% methane
Kr counter gas: 20-30 μl krypton + 100% methane

## Slide 12
39Ar detection: low background proportional counting tubes
Gran Sasso (Italy)?
A salt mine? A cave or a vine cellar in Hungary?

## Slide 13
39Ar detection: low background proportional counting tubes
A salt mine? Turda (Romania), Prahova (Romania)?
A vine cellar?

## Slide 14
39Ar detection: low background proportional counting tubes
Slanic Prahova

## Slide 15
39Ar detection: low background proportional counting tubes
Slanic Prahova

## Slide 16: Rb-Sr rendszer
Rb: alkali; soluble, mobile, highly incompatible, substitutes for K
Sr: alkaline Earth; soluble, somewhat mobile, incompatible, substitutes for Ca
Both concentrated in the Earth’s crust; particularly Rb. High Rb/Sr in granitic rocks and their derivatives.

## Slide 17: Sr kronoszratigráfia
Sr present in relatively high concentration is seawater.
Also concentrated in carbonates (abundant marine bio-sediment).
Long residence time; therefore
  Sr isotopic composition of open ocean water is uniform (in space).
Sr isotope ratio varies in time, mainly due to changes in the relative fluxes from the continents (erosion) and mantle (ridge-crest hydrothermal activity).
Particularly in the Tertiary, Sr isotope ratio of marine sediment can be used to date the horizon..

## Slide 18: Az urán és bomlási sora

## Slide 19: Sr-U izotóparány paramétertér
Figure 2.12

## Slide 20
Neptune Plus: multicollector inductively coupled plasma ion source mass spectrometer
17 ppm
14 ppm
Wet plasma 100 ppb 87Sr/86Sr
Wet plasma 100 ppb 87Sr/86Sr

## Slide 21
Neptune Plus: multicollector inductively coupled plasma ion source mass spectrometer
0.49 %
0.43 %
0.77 %
0.48 %

## Slide 22
Vízmintavételi helyszínek (ROHU projekt)

## Slide 23: Sr-U izotóparány paramétertér

## Slide 24: Preparálás 1. (Platzek et al., 2016)
UTEVA gyanta, előre töltött
100 ppb U oldat (ICP koncentráció std), 15 mL
Gyanta előkezelése: 4 M HNO3, 5 BV (BV=bed volume; 4 mL), majd öblítés UTV-zel, közvetlenül a használat előtt
Kondicionálás: 4 M HNO3, 3 BV
Minta felvitele
Mátrix elúció: 5 BV 4 M HNO3
Minta gyűjtése: 5 mL 0,02 M HNO3/0,0005 M HF
A teszt során 1, ill. 2 mL-es frakciókat szedtünk. Ezeket kétszer bepároltuk tömény HNO3-ban (ultrapure), majd 3 %-os salétromsavban vettük fel.
Preparálás 2. (Stoliker et al., 2013)
AG 1x8 anioncserélő gyanta, 2 mL
Kondicionálás: 30 mL 8 M HCl
Minta felvitele: A) 7,5 mL 200 ppb urán oldat a gyantára; B) 7,5 mL 200 ppb urán oldat bepárolva, 3x1 mL cc. sósavval újból bepárolva, majd 1 M HCl-ban felvéve és a gyantára adagolva
Mátrix lemosás: 8 M HCl, 5x3 mL
U eluálás: 1 M HCl, 5x3 mL
Mosás: 5x3 mL UTV
A 2x4 frakciót bepároltuk, 3x1 mL tömény salétromsavban újból pároltuk, majd 3 %-os salétromsavban vettük fel.

## Slide 25
SEC - size exclusion chromatography
Chart: Sr elválasztás Spec-gyanta (SEC)
Sr | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0043 | 0.1139 | 0 | 0 | 0 | 0 | 0
Rb | 0 | 0.012 | 0.045 | 0.038 | 0.002 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sr (mg/l)
Frakció 2ml-ként, db

## Slide 26
Sr tartalmazó frakció bepárlása és salétromsavas roncsolása (Ultratiszta 69% HNO3)
Sr oszlopkromatográfiás elválasztása,
akár 50ppb koncentrációjú oldatból kiindulva

## Slide 27
Neptune Plus: multicollector inductively coupled plasma ion source mass spectrometer

## Slide 28
Neptune Plus: multicollector inductively coupled plasma ion source mass spectrometer

## Slide 29: Sampling in South Africa
5-20 Oct 2019

## Slide 30
Buffels River Valley
Cape Winelands

## Slide 31
Hard work….

## Slide 32
Buffels River Valley

## Slide 33
….the lowest flow rate

## Slide 34
A recharge are in middle-Hungary (3H/3He dating)

## Slide 35
Western Cape, South-Africa (3H/3He dating)

## Slide 36
Palaeoclimate reconstruction: Great Hungarian Plain, Hungary
9.1 ± 0.8 °C

## Slide 37
Kucaj-Beljanica Karst, Serbia
M7000 years!

## Slide 38
Methods for water age detemination
(time range: 0 to many millions of years)